## Slide 1: Electronics Workshop
2017 June 30
Arduino Week (3)

## Slide 2: Files to Cover
Works_017_a
  Bitwise operation
Works_017_b
  Quick look at I2C with Arduino
Works_018_a
  Library file building
Works_018_b
  Library file building by self

## Slide 3: Why I2C? (UART)
Asynchronous; no clock data is available
Each end-device must agree on data rate
Each end-device must have close-to same clock rate as well
Requires 10 bits to send 8bits of data; for start and stop bit.
Designed only for two devices
Limited data rate compare to I2C

## Slide 4: Why I2C? (SPI)
Requires more pin compare to I2C
  MISO
  MOSI
  SCK
  CS
One additional slave device = One additional CS pin on I/O
Designed only for one master
Compare to I2C however, data rate is much faster (~10MHz)

## Slide 5: And now… the I2C!
Two wires only!
  SDA: Signal Data
  SCL: Signal Clock
Technically, with two wires, can connect up to 1008 slave devices!
Supports multiple Masters!
Faster than UART, slower than SPI
  100kHz~400kHz